## Slide 1: Background
Graham Peyton

## Slide 2: A bit about me
Grew up in Johannesburg, South Africa, got married there and now have 3 daughters!
Move to London for PhD in 2014
Research led me to US @ Butterfly in 2017
Been at 4C since then, currently at Liminal working on ultrasound BCI
Hobbies: fingerstyle guitar, pickleball/tennis

## Slide 3: Educational background
Double major in SA (2008-2012)
  Biomedical and EE
MSc (2013)
  computational neuroscience
  Magnetoencephalography - parity detection
  Focused on multivariate signal processing – ICA/PCA, wavelets, time-frequency, topographical mapping.
PhD (2014-2017)
  Full-stack dev of ultrasound system, including full custom AFE

## Slide 4: Ultrasound background

## Slide 5: PhD @ Imperial College London
Main objectives:
Build architecture “ultra-miniaturized” ultrasound – low power for wireless
Build proof-of-concept HW, including on-chip AFE

## Slide 6: AFE in 0.35um CMOS

## Slide 7: Beamformer
The beamformer is implemented on a Spartan-6 FPGA - consumes 296mW for a frame rate of 7Hz.

## Slide 8: Imaging Results
SNR/resolution limited by #transmits

## Slide 9: Log-domain in BiCMOS

## Slide 10: Some fun with digital
On-chip implementation of beamformer – started synthesis/physical layout, but never taped out.
Integration with transducer, packaging etc.

## Slide 11: Butterfly
8960 Elements:
Independent Receiver
and Transmitter
1120 Channels:
Independent ADC
and Gain Control
140 Ultrasound Processing Units:
Digital Signal Processing
8960 Individual
Sensor Elements
Matrix Array:
Sensor and Analog Front-End
Ultrasound Processing Units
Ultrasound Processing Units
31.0mm
20.0mm
Notes: What is the frequency range of operation vs. size relation for CMUT? [NS on CMOS]
  Lambda/2 at ~4MHz (enables phased array operation)
  Lambda pitch at ~8MHz (enables linear operation)
What is/are your drive voltage/voltages? [NS on CMOS]
  Today: Pulser: 40V AC
  Today: VBias: ~60V DC
What is the minimum receive signal and the dynamic range of the received signal? [NS on CMOS]
  Per CMUT element: 1.6Pa => 4kPa (high gain mode) or 4.3Pa => 31.4kPa (high DR mode) **NS TO FIX**
What is the data rate coming out of the 2D array at full operation? [NS on CMOS]
  280Gbps from ADCs
What is the resolution and pitch in x and y for the 2D array? [NS on CMOS]
  208um pitch for both dimensions.
What is the main benefit for you for using a 2D array instead of a linear array? [NS on CMOS]
  Universal Probe! Configurable aperture size, elevational beamforming.
  (Bonus: low frame rate 3D)

## Slide 12: Initial Contributions
Started out designing BIST circuitry for existing AFE
Helped with optimization of transmitter circuitry
LVDS transmitter
Developed a few patents on new data processing/beamforming techniques targeting wireless, covering hardware, algorithms and software – see scholar

## Slide 13: Non-volatile memory - eFuse

## Slide 14: SerDes, SI/PI, modeling, package design, etc
Designed serializer + NRZ transmitter
Next-gen packaging – analog/digital stack
  Design and modeling
Left before tapeout

## Slide 15: Liminal
Team lead on all things HW
Contributions
  Designed entire architecture – full ultrasound AFE, FPGA beamformer, imaging / AI backend, comms link, etc
  Designed 90% of schematic, handed over layout to full time EE
  Imaging/SW: ported color flow pipeline from Python  GPU in C++, performed benchmark tests.
  Bringup, verification, EMC testing, 60601 conformance
  Key contributor + support for thermal / housing solution
  Manufacturing, supply chain, scheduling, etc
Managed 2 full-time EEs and 3 consultants (FPGA, EE)